## Slide 1: QUS Toolbox
Theresa H. Lye
3/29/2021

## Slide 2: QUS Toolbox
These codes were adapted from Daniel’s software and the majority of the main algorithms are the same (e.g. computation of Faran sphere form factor is the same; computation of effective scatterer size and effective acoustic concentration from Gaussian fit are the same).
The difference is that the code has been re-organized. MATLAB objects are no longer used and are replaced with structs. The code is hopefully easier to interpret and adapt this way.
This PowerPoint will guide you through the example, ProcessQUS_example.m, in the EXAMPLE folder. Each slide covers different parts of the ProcessQUS_example.m script.

## Slide 3: 1. Add path to BSC toolbox
Edit the path as needed.

## Slide 4: 2. Inputs
Specify the folders containing your reference and sample data (.mat files), and the names of the files.

## Slide 5: 3. ROI Info
The QUS parameters will be calculated in overlapping ROI, and the roi struct contains your desired ROI specifications.
  roi.len_x/y/z = the length of each ROI
  roi.o_x/y/z = the amount of overlap between ROI (in %)
If you don’t want to process the entire image volume, you can specify a sub-region of the image volume in which to generate the overlapping ROI:
  roi.init_x/y/z = starting point for ROI
  roi.end_x/y/z = ending point for ROI
Note that I typically specify distance in meters throughout the code. You can probably adjust as needed, but something to keep in mind…

## Slide 6
Here is a B-mode and a C-scan with the ROI plotted on them (from the example).
If you set the following (in meters)…
roi.init_z = 6*1e-3;
roi.end_z = 11*1e-3;
roi.init_x = 6*1e-3;
roi.end_x = 8*1e-3;
QUS parameters will only be extracted from inside the red box, which has dimensions of X = 6 mm to 8 mm; Z = 6 mm to 11 mm.
This is just a zoom in of the upper left corner of the box in the above subplot. The yellow, blue, and green boxes show 3 representative ROI.
roi.len_x = 1.0*1e-3;
roi.len_z = 0.6*1e-3;
roi.o_x = 50;
roi.o_z = 50;
The ROI are each 1.0 mm in X, and 0.6 mm in Z. They overlap by 50% in each direction.
roi.init_y and roi.end_y were not set… so, the code automatically processes the full y-dimension of the image volume.
roi.len_y = 2.0320e-04 , roi.oy = 0
The length of one ROI in y covers one plane, no overlap. So we’re processing each plane individually.

## Slide 7: 4. Spectrum Info
Set your desired FFT-padding and the transducer bandwidth.

## Slide 8: 5. Reference and Compensation Parameters
Parameters to compute the theoretical reference BSC, attenuation compensation, and transmission compensation are specified here.
The .mat files contain structs holding the necessary parameters.
They also contain a ‘description’ struct that should tell you what each variable is.

## Slide 9: For example, for ph_18.mat (18 um phantom, parameters for theoretical BSC)
ph_18 | description
a: 9.099999999999999e-06 | 'Scatterer radius [m]'
c1: 5640 | 'speed of sound in scatterer [m/s]'
c0: 1500 | 'speed of sound in medium [m/s]'
n: 1.560000000000000e+12 | 'average particle number density [particles/m^3]'
gamma: 8.400000000000000 | 'relative acoustic impedance between scatterer and surrounding medium'
poisson: 0.200000000000000 | 'poisson'
pwire: 2.500000000000000 | 'scatterer density [g/cm^3]'
ph2o: 1 | 'medium density [g/cm^3]'
Nume: 20 | 'number of iterations to compute scattering theory'
The ph_18.mat file was created from GeneratePhantomObj.m. Feel free to create more .mat files if you have other phantoms…

## Slide 10: 6. Specify desired parameters to save
Here, simply list some names for parameters you want to save.
You can put anything you want in this cell array.
It’s really just for your own reference later.
e.g. params{1} = 'HK Structure Param‘… so later on, result{1} will be set to HK Structure Parameter maps.

## Slide 11: 7. Setup reference
Here, load your reference data and set up its theoretical BSC, attenuation compensation, and transmission compensation parameters.
Creating the ref struct using loadData.m
  This function creates the struct that will hold all the important information for your reference.
  You need to edit loadData.m to fill in the appropriate fields based on the data that you loaded from your .mat file.
Afterwards, the ref struct gets appended with the BSC and compensation parameters.

## Slide 12: You need to fill in the following fields for your ref struct by editing loadData.m.
data: [13312×256×10 double] | RF data volume
env: [13312×256×10 double] | Envelope of RF data volume
x: [1×256 double] | X coordinates, in meters
y: [1×10 double] | Y coordinates, in meters
z: [1×13312 double] | Z coordinates, in meters
dx: 5.521568627450981e-05 | Resolution of X coordinates, in meters
dy: 2.032000000000000e-04 | Resolution of Y coordinates, in meters
dz: 7.519531250000000e-07 | Resolution of Z coordinates, in meters
c: 1540 | Speed of sound to convert time to Z (m/s)
t: [1×13312 double] | Time coordinates, in seconds
fs: 1.024000000000000e+09 | Sampling rate (Hz)

## Slide 13: 8. Setup sample
Here, you load and setup your sample data, similarly as you did for the reference.
For this example, I also included a .mat file that contains the indices of this sample’s surface, used later for attenuation compensation.

## Slide 14: 9. Generate ROI
The indices of all ROI get created with genROIpos.m, outputs all_roi and all_roi_idx.
plotROIonBmode.m plots the figure from slide 6.

## Slide 15
len_x: 1.000000000000000e-03 | These are the ROI parameters that were initially specified in the input roi struct.
len_y: 2.032000000000000e-04 | 
len_z: 5.999999999999999e-04 | 
o_x: 50 | 
o_y: 0 | 
o_z: 50 | 
init_z: 0.006000000000000 | 
end_z: 0.011000000000000 | 
init_x: 0.006000000000000 | 
end_x: 0.008000000000000 | 
init_y: 0 | Because roi.init_y and roi.end_y weren’t specified as input, they were automatically filled to the full image volume dimensions
end_y: 8.128000000000000e-04 | 
step_x: 4.959686888454012e-04 | The distance between adjacent ROI.
step_y: 2.032000000000000e-04 | 
step_z: 3.000292968750000e-04 | 
pos_x: [1×3 double] | The starting position of each ROI along each dimension (total number of ROI over image volume = 3 x 5 x 15).
pos_y: [1×5 double] | 
pos_z: [1×15 double] | 
The all_roi struct that gets output from genROIpos.
all_roi_idx is basically the same, except everything is in units of MATLAB indices instead of meters.

## Slide 16: 10. Compute QUS parameters for each ROI
Here we compute parameters for each ROI.
Parameters will be stored in the result cell array.

## Slide 17: Extract the RF data for the ROI, getROI.m
Check the comments at the top of the function for instructions.
Also notice that we’re using the full lateral dimensions for the reference ROI each time (only matching depth).
Also see how we are saving the parameters:
result{param2idx(params,'XCoord')}(k,i,j) = mean(samp.sub_vol.x);
param2idx outputs the index of the given string in the params cell array… so result{10} = matrix with average X location of each ROI

## Slide 18: Compute BSC and QUS parameters
You can check each function for descriptions of the inputs and outputs.

## Slide 19: 11. Plot the Parameter Maps
Here, each of the parameters maps for the one plane that was processed are plotted.
The units are given in the titles.
Note: The units of the Nakagami scaling factor, effective scatterer size, and HK scattering clustering parameter were modified before plotting (see convertUnits.m).

## Slide 20
This should be your output.